## Slide 1: VoltMesh
Offline safety network for e-micromobility
SHIFT Hackathon · IIT BHU · 10–11 October 2026
Project overview: what we built and why
Notes: VoltMesh is an offline safety network for electric two-wheeler riders. Phones and battery-swap stations form a mesh; a station phone with internet is the gateway to the backend. Built for the SHIFT hackathon at IIT BHU.

## Slide 2: Riders get stranded, offline
Battery runs out far from a station
Nowhere to charge, often no signal to call
Battery thermal event
Overheating or fire: seconds matter
Crash
The rider may not be able to reach the phone
Network dead zone
Underpasses, basements, highway stretches
Prepaid data runs out
Common for gig workers; same as a dead zone
Fear of being stranded slows the switch from petrol.
A safety net that works with no signal removes that barrier, without building towers.
Failure frequencies are not yet sourced, so we quote none.
Notes: EV riders, especially delivery riders, fail in ways a petrol rider does not, and often where networks are weakest. We do not quote failure statistics because we have no sourced numbers yet.

## Slide 3: Daily use first, safety on top
1 Offline battery stock
Stations broadcast what is in stock. Phones relay and cache it, so riders see batteries with no signal.
2 Stranding prevention
Rider sets battery %. If no station in range has stock, a warning goes out before they are stranded.
3 SOS relay
Stranded, crash, battery fire or other. The alert hops from rider to rider to a station.
An SOS-only mesh never reaches density, because nobody keeps an app open for a rare emergency. Finding batteries daily keeps phones on, and each one is a relay.
Notes: The key insight: an SOS-only mesh has a cold-start problem. If riders keep the app on every shift to find charged batteries, every phone becomes a relay for someone else's SOS.

## Slide 4: How it works
Rider phones
Relay alerts over Bluetooth
Swap station
Gateway: the only part that needs internet
Backend
Supabase database + API on Render
Admin portal
Live map, alerts, stock, vehicles
Scooter unit
Reports battery and events, asks for holds
Bluetooth carries discovery and a 24-byte alert. Wi-Fi Direct carries bigger payloads. Only the station needs internet.
Any unit that can send HTTPS can join
Notes: Phones relay over Bluetooth, the swap station is the gateway with internet, the backend stores everything and the admin portal reads it. Scooters can also talk to the backend directly through the vehicle API.

## Slide 5: What we built
Backend
Live
Database, 6 API functions, access rules and battery holds on Supabase and Render.
Admin portal
Live
Role login, live map, alerts, stations, vehicles and a Bluetooth page.
Vehicle API
Live, tested
Scooters report battery and events, find stations and reserve batteries.
Phone app
UI only
Screens exist but no real Bluetooth yet. Needs a development build.
8 + 1
tables and one view
6
API functions
7
database migrations
Notes: Backend, admin portal and vehicle API are live. The phone app is UI only: no real Bluetooth yet. Counts: eight tables and one view, six API functions, seven migrations.

## Slide 6: Backend and database
provision
Gives a phone or station its ID
ingest
Takes packets from a gateway and checks signatures
sos
Direct SOS from a rider with internet
vehicle
Scooter API: battery, events, holds
admin
Portal actions: holds, stock, vehicles
help
A rider offers to help a stranded peer
PostgreSQL on Supabase
alerts
stations
relay_hops
vehicles
vehicle_telemetry
reservations
help_offers
riders
PostGIS
Row-level security
Realtime
Storage
Notes: One Postgres database in Supabase with PostGIS. Six small API functions. The same function code runs on Supabase Edge Functions and on a Node service on Render.

## Slide 7: Admin portal
Live map
Dark or light map, alert clusters, stations with stock and a relay path line.
Alert response
Filter alerts, mark help sent or resolved, and hold a battery at a station.
Stations and stock
Plus and minus stock buttons. Held batteries are counted out automatically.
Road routes
OSRM routes to the nearest stations with stock, checked against battery range.
Vehicles and keys
Register scooters, issue and rotate API keys, set each range profile.
Bluetooth devices
Scan, connect and read nearby low-energy devices from the browser.
Notes: A React and Leaflet web app on GitHub Pages. Roles are admin, fleet and station. Row-level security in the database enforces what each role can read and change.

## Slide 8: Plug into any scooter
POST
/v1/telemetry
Battery %, temperature, position. Runs the range check.
POST
/v1/events
Crash, stranded, thermal or other.
GET
/v1/stations/nearby
Stations with batteries available.
POST
/v1/reservations
Ask a station to hold a swappable battery.
Three ways in
Telematics unit on the scooter
Rider's phone as a bridge
A fleet's existing back office
Reading a scooter's battery needs an adapter per maker. This API is the stable target it posts to.
Notes: The vehicle API is small on purpose: anything that can make an HTTPS request with a key can integrate. Reading the scooter battery itself needs a per-maker adapter outside this repo.

## Slide 9: Stranding protection
usable range = battery % × km per % × (1 − safety margin)
1
Check range
The scooter reports battery and position. The server finds stations with stock inside usable range.
2
Warn early
If none is reachable, a low-battery alert is raised, once, before the rider is stranded.
3
Hold a battery
A station is asked to hold a swappable battery. Stock drops while held, then it expires.
Range is a heuristic from a per-scooter figure, not a measurement. The phone app uses 1.2 km per % today.
Notes: The range check is a heuristic: battery percent times kilometres per percent times one minus a safety margin. The phone app currently uses a fixed 1.2 km per percent; the backend uses a per-vehicle value with no default.

## Slide 10: Algorithms and method
No machine learning: deterministic rules that can be explained and verified.
Range check
Battery % × km per % × (1 − margin) against stations with stock
Haversine distance
Great-circle distance between two coordinates
HMAC-SHA256 tag
A 3-byte signature that fits the 24-byte Bluetooth packet
Duplicate handling
Random alert ID as the key, so mesh and direct copies merge
Controlled flooding
Drop seen or expired packets, add a hop, rebroadcast (designed, not yet on phones)
Spatial clustering
Zoom grid and DBSCAN in PostGIS keep the map readable
Atomic battery holds
Station row is locked so two riders cannot claim the last battery
OSRM road routing
Shortest road path on OpenStreetMap, used for station routes
Notes: There is no machine learning: everything is deterministic and can be checked. The controlled flooding is specified and unit-testable but is not yet running on real phones.

## Slide 11: Tested on the live system
33.6 km
usable range at 42% battery; both test stations reachable
0.8 km
usable range at 1% battery: no station in range, alert raised
3 → 2
station stock while a hold is active; back to 3 after cancel
409
a second hold from the same vehicle is refused
Also verified: input validation, wrong-key and no-login rejections, forged-packet rejection.
Test setup: one test vehicle (1 km per %, 20% margin) and one test station. Test inputs, not field measurements.
Notes: These are results from one test vehicle and one test station on the live project, with test inputs of one kilometre per percent and a twenty percent safety margin. They are not field measurements.

## Slide 12: Safety: built and not built
Working
Low-battery alert from the range check
Battery holds with stock counting
Crash, stranded and thermal events from a vehicle
Role-based access and key checks
Forged mesh packets rejected
Not built yet
Offline Bluetooth relay and one-tap SOS on phones
"I can help" on nearby phones (backend is ready)
Automatic crash detection
Notifications to the fleet: text, email, push
Escalation if an alert is ignored
Notes: Safety works today as an online alert and response system. The offline Bluetooth mesh, which is the demo's core, is not built yet. Nothing yet notifies the fleet outside the portal.

## Slide 13: Honest limits
Offline mesh not built yet
No real Bluetooth transport, so no measured delivery rate.
Demo-grade security
One shared key, an open sign-up endpoint, no replay or rate limits yet.
Battery % is typed in
Reading a scooter's battery needs a per-maker adapter.
Range is a heuristic
Real range varies with load, speed and terrain.
Android only
iPhones cannot relay in the background.
Location is plaintext
Alerts carry rough position over Bluetooth; we disclose it.
Notes: We state the limits plainly. Demo-grade security is disclosed as such, and we only claim what our own recorded runs measure.

## Slide 14: What's next
Now
Lock down the sign-up endpoint
Reject old and replayed packets
Fleet notifications for new alerts
Test a signed SOS end to end
Next
Phone app development build
Bluetooth test: phone A to B
Three-phone relay with relay log
10+ recorded demo runs
Later
Per-device keys
Read scooter battery over Bluetooth
Road-condition sharing
Wi-Fi Direct payloads
Notes: Priorities: first close the security gaps and add notifications, then build the real Bluetooth relay, which is the core of the demo, then harden for production.

## Slide 15
Daily use first. Safety rides on it.
VoltMesh
Portal: aravworks.github.io/SHIFT-2026-P83EUY
Code: github.com/aravworks/SHIFT-2026-P83EUY
Notes: Close: everyday value first, safety rides on it. Offer the live portal and the repository.